## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Good Representations and Modular Arithmetic

## Slide 2: What About Negative Numbers?
Last time, we developed
  the N-bit unsigned representation
  for integers in the range [0, 2N – 1]
Now, let’s think about negative numbers.
  How should we represent them?
  Can we use a minus sign?
–11000 = –2410 ?
There’s no “–” in a bit!

## Slide 3: One Option: The Signed-Magnitude Representation
But we can use another bit for a sign:
0 → +, and 1 → –
Doing so gives the N-bit signed-magnitude representation:
This representation can represent numbers in the range [-2N-1 – 1, 2N-1 – 1].
sign
(N-1)-bit magnitude

## Slide 4: What Happened to the Last Bit Pattern?
Signed-magnitude was used in some early computers (such as the IBM 704 in 1954).
A question for you:
  The range represented is [-2N-1 – 1, 2N-1 – 1].
  That gives 2N – 1 different numbers.
  What’s the last pattern being used to represent?

## Slide 5: Signed-Magnitude Has Two Patterns for Zero
There are two bit patterns for 0!
This aspect made some hardware more complex than is necessary.
Modern machines do not use signed-magnitude.
0
00000…00000
1
00000…00000
+0
-0

## Slide 6: How Do We Choose Among Representations?
What makes a representation good?
  efficient: most bit patterns represent some item uniquely (so, not unary! )
  easy/fast implementation of common operations: such as arithmetic for numbers
  shared implementation with other representations: in this case, implementation is “free” in some sense
Notes: Point out that it’s not a fair question, because they don’t know enough to give all of the answers. In particular, the second answer requires knowledge of hardware design. However, they should be able to understand why the third answer is good if we can achieve it (which we do with addition/substraction of unsigned and 2’s complement).

## Slide 7: Representations Can be Chosen to Share Hardware
Imagine a device that performs addition on two bit patterns of an unsigned representation.
Can we use the same “adder” device for signed numbers? Yes! If we choose the right representations.
unsigned
adder
0
1
0
“2”
0
1
1
“3”
1
0
1
“5”

## Slide 8: Add Unsigned Bit Patterns Using Base 2 Addition
Recall that the unsigned representation is drawn from base 2.
We use base 2 addition for unsigned patterns.
  Like base 10, we add digit by digit.
  Unlike base 10, the single-digit table of sums is quite small…
  What is 1 + 1 + 1?
A | B | Sum
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
10
11
Notes: 10 kinds of people in the world: those who understand binary, and those who don’t. Sorry.

## Slide 9: Example: Addition of Unsigned Bit Patterns
Let’s do an example with 5-bit unsigned
01110 (14)
+ 00100 (4)
Good, we got the right answer!
0
1
1
1
0
1
0
(18)

## Slide 10: Overflow Can Occur with Unsigned Addition
The unsigned representation is fixed width.
  If we start with N bits,
  we must end with N bits.
What is the condition under which the sum cannot be represented?
  The sum should have a 1 in the 2N place.
  Only occurs when the most significant bits of the addends generate a carry.
We call this condition an overflow.

## Slide 11: Example: Overflow of Unsigned Bit Patterns
Let’s do an another example, again with 5-bit unsigned
01110 (14)
+ 10101 (21)
Oops! (The carry out indicates an overflow for unsigned addition.)
1
1
1
0
1
0
(3)
0
1
We have no
space for
that bit!
Notes: Remember that 14 + 21 = 3 for your exams!

## Slide 12: Unsigned Addition is Modular Arithmetic
Modular arithmetic is related to the idea of the “remainder” of a division.
Given integers A, B, and M,
  A and B are said to be equal mod M iff*
  A = B + kM for some integer k.
Note that k can be negative or zero, too.
We write: (A = B) mod M.
* “iff” means “if and only if,” an implication in both directions, and is often used for mathematical definitions
Notes: Students should recall remainders from elementary school.

## Slide 13: Unsigned Addition is Always Correct Mod 2N
Let SUMN(A,B) be the number represented by the sum of two N-bit unsigned bit patterns.
If no overflow occurs (A + B < 2N), we have SUMN(A,B) = A + B.
For sums that produce an overflow, the bit pattern of the sum is missing the 2N bit, so SUMN(A,B) = A + B – 2N
In both cases, (SUMN(A,B) = A + B) mod 2N.

## Slide 14: Modular Arithmetic Key to Good Integer Representations
Modular arithmetic is the key.
It allows us to define
  a representation for signed integers
  that uses the same devices
  as are needed for unsigned arithmetic.
The representation is called 2’s complement.
Details soon…

## Slide 15: Modular Arithmetic on the Number Line
To understand modular arithmetic graphically, imagine breaking the number line into groups of M numbers, as shown above for M=8.
Two numbers are equal mod M if they occupy the same position in their respective groups.
For example, 0 is equal to an infinite number of other numbers (…, -24, -16, -8, 8, 16, 24, …).
We usually name sets of numbers that are equal mod M using the number in the range [0, M-1].
0
7
8
15
-8
-1
Notes: NOTE THAT THIS SLIDE IS HIDDEN—IT IS NOT POLISHED ENOUGH FOR PRESENTATION.

## Slide 16: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Signed Integers and 2’s Complement

## Slide 17: Strategy: Use Common Hardware for Two Representations
Recall:
  addition of bit patterns in N-bit unsigned representations
  corresponds to arithmetic mod 2N.
Using this arithmetic, we develop the 2’s complement representation for signed integers.
The same hardware can then perform arithmetic for both representations.
What about the name? Later.

## Slide 18: Graphical Illustration of Modular Arithmetic
The circle illustrates 3-bit unsigned.
Adding a number corresponds to counting clockwise.
The answer is always correct mod 8.
(For subtraction, count the other way.)
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
+3
Notes: Explain the connection between the represented value (outside) and the bit pattern (inside).

## Slide 19: Representations Must be Unambiguous
The same circle illustrates equality mod 8.
For example, we can extend the numbers in a clockwise direction.
Or the other way.
Overflow occurs because a representation can have only one value per bit pattern.
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
, 9
, 8
, 10
, 11
, 12
-1,
-2,
-3,
-4,
Notes: Point out that labels at any point on the outside are all equal mod 8 (for example, -4 = 4 = 12 mod 8).

## Slide 20: We Can Choose Any Meaning for a Bit Pattern
But what if we pick a different set of labels?
The arithmetic doesn’t change.
Let’s include both positive and negative numbers!
And try some addition.
0
1
2
3
-3
-2
-1
000
001
010
011
100
101
110
111
+3
Notes: Don’t talk about the bottom label yet (4 or -4). Can do > 1 addition, illustrate overflow, and so forth.

## Slide 21: That’s One Way to Define 2’s Complement
Draw a circle for N bits (2N points).
Starting at 0 at the top.
Write unsigned bit patterns clockwise around the circle.
Starting again from 0,
  find bit patterns for negative numbers
  by moving counter-clockwise.
What about the name? Later.

## Slide 22: 2’s Complement Can Also be Derived Algebraically
We can also define N-bit 2’s complement algebraically.
An adder for N-bit unsigned gives
SUMN(A,B) = A + B mod 2N
N-bit 2’s complement includes positive numbers in the range [1, 2N-1 – 1]. These bit patterns all start with a “0” bit.
We need to find bit patterns for negative numbers.
Notes: Mention to the students that the two derivations are completely equivalent. We present both because some students find one easier than the other. If a student understands one of the two, that’s good enough.

## Slide 23: Properties Needed for Negative Number Bit Patterns
For each number K, 0 < K < 2N-1,
  we want to find an N-bit pattern PK, 0 ≤ PK < 2N,
  such that for any integer M,
(-K + M = PK + M) mod 2N
The bit pattern PK then produces the same results as -K when used with unsigned arithmetic.
Also, PK must not be used by a number ≥ 0.

## Slide 24: Do Algebra to Define Negative Patterns
Starting with our property,
(-K + M = PK + M) mod 2N,
subtract M from both sides to obtain
(-K = PK) mod 2N.
Next, note that
(2N = 0) mod 2N.
Now add the last two equations to obtain
(2N – K = PK) mod 2N.

## Slide 25: Final Answer: -K is Represented by 2N – K
One easy solution to (2N – K = PK) mod 2N is PK = 2N – K.
Since 0 < K < 2N-1, this solution gives 2N-1 < PK < 2N.
But these are all unused bit patterns—the patterns starting with “1!”
So we’re done: -K is represented by the pattern 2N – K.
What about the name? Are you really ready?

## Slide 26: Negating Twice Gives an Identity Operation
Let’s do a sanity check.
What is the bit pattern for - (-K)?
We know that -K is 2N – K.
Substituting once, we obtain - (2N – K).
Substituting again, we obtain 2N – (2N – K).
But that’s just K, as we expect.
What name? Oh, “2’s complement?”

## Slide 27: Is There an Easy Way to Find -K?
How do we calculate 2N – K?
We can subtract (for example, with N=5)…
100000 (2N)
- ????? (K)
But that seems painful.
Instead, notice that 2N = (2N – 1) + 1.
So we can calculate (2N – 1) – K + 1.

## Slide 28: 2’s Complement is 1’s Complement Plus One!
Again for N=5:
11111 (2N – 1)
- ????? (K) (answer)
+ 1
The first step is trivial: replace 0 with 1, and 1 with 0. The result ((2N – 1) – K) is called the 1’s complement of K.
Adding 1 more gives the 2’s complement.
Notes: Haha. Engineers are so funny.

## Slide 29: Distinguish 2’s Complement from Negation
Here or elsewhere, you will hear the phrase “take the 2’s complement.”
We will try not to use “2’s complement” in that way.
Students get confused between the 2’s complement representation for signed integers and the operation of negation on a bit pattern for a number represented with 2’s complement.
For clarity, we suggest that you do the same.

## Slide 30: Example: Negating a Number in 2’s Complement
Let’s do an example of negation with 8-bit 2’s complement.
As you know, I like 42.
As you may remember, 4210 = 00101010.
So what’s -42?
First, complement the bits: 11010101.
Then add 1: 11010110 = -4210!

## Slide 31: 2’s Complement Conversion Can Be Same as Unsigned
For non-negative numbers (bit patterns starting with 0),
conversion between decimal value and 2’s complement bit pattern
is identical to conversion for the unsigned representation.

## Slide 32: Use Two Negations to Convert Negative Numbers
To convert decimal D < 0 to 2’s complement,
  first convert –D (as unsigned),
  then negate the resulting bit pattern.
To convert a negative 2’s complement bit pattern (a bit pattern starting with 1) to decimal,
  first negate the bit pattern,
  then convert to decimal D (as unsigned).
  The answer is -D.

## Slide 33: Alternate Method for Calculating 2’s Complement Values
If we have a negative number -K, we can use the base 2 polynomial to calculate 2N – K:
2N – K = aN-12N-1 + aN-22N-2 + … + a020
We know that aN-1 = 1 for a negative number. Substituting and subtracting 2N gives:
-K = (2N-1 – 2N) + aN-22N-2 + … + a020
-K = -aN-12N-1 + aN-22N-2 + … + a020
This polynomial also works when aN-1 = 0.

## Slide 34: What about the Last Bit Pattern?
We didn’t define a value for one of the bit patterns!
What should it be?
2N-1?
In 2’s complement, the pattern always means -2N-1.
Why? So that any pattern starting with a 1 is negative!
0
1
2
3
4
-3
-2
-1
000
001
010
011
100
101
110
111
-4,
-2N-1?
Undefined?
Notes: Ask the students to explain why before revealing the answer.

## Slide 35: Extend Unsigned Bit Patterns by …
In some cases, we need
  to convert a bit pattern
  from a smaller representation (fewer bits)
  to a larger one (more bits)
How do we convert N-bit unsigned to (N+k)-bit unsigned (for k > 0)?
Hint: We already had to solve a similar problem when a number does not require N bits in base 2.
Add k more leading 0s (called zero extension).
Notes: NOTE: This slide was added for class. Maybe skip in microlectures?

## Slide 36: What about 2’s Complement?
How do we convert N-bit 2’s complement to (N+k)-bit 2’s complement (for k > 0)?
For non-negative values,
  2’s complement is the same as unsigned (with an extra 0 for the sign)
  So add k more leading 0s.
What about negative values?
Notes: NOTE: This slide was added for class. Maybe skip in microlectures?

## Slide 37: Extend 2’s Complement Bit Patterns by …
In 5-bit 2’s complement,
-510 has bit pattern 11011
-1010 has bit pattern 10110
And in 8-bit 2’s complement?
-510 has bit pattern 111 11011
-1010 has bit pattern 111 10110
So how do we convert N-bit 2’s complement to (N+k)-bit 2’s complement (for k > 0)?
Add k copies of the sign bit (called sign extension).
(spaces added to
help us humans)
Notes: NOTE: This slide was added for class. Maybe skip in microlectures?