## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
2’s Complement Overflow and Boolean Logic

## Slide 2: Example: Addition of Unsigned Bit Patterns
A question for you:
What is the overflow condition for addition of two N-bit 2’s complement bit patterns?
(That is, when is the sum incorrect?)
Remember that addition works exactly the same way as with N-bit unsigned bit patterns, so we can do some base 2 addition to find the answer.

## Slide 3: Adding Two Non-Negative Patterns Can Overflow
Let’s start with our first example from before:
01110 (14)
+ 00100 (4)
Oops! We had no carry out, but the answer is wrong (an overflow occurred).
So overflow is different than for unsigned…
0
1
1
1
0
1
0
(-14)

## Slide 4: Carry Out Does Not Indicate 2’s Complement Overflow
This example overflowed when the bits were interpreted with an unsigned representation.
01110 (14)
+ 10101 (-11; 21 unsigned)
But here the answer is still correct!
Carry out ≠ overflow for 2’s complement.
1
1
1
0
1
0
(3)
0
1
We have no
space for
that bit!
Notes: The bits and the addition are IDENTICAL. Only we “know” whether we should interpret the bits as unsigned or 2’s complement.

## Slide 5: Adding Non-Negative to Negative Can Never Overflow
Claim:
Addition of two N-bit 2’s complement bit patterns can not overflow if one pattern is negative (starts with 1) and the other pattern is non-negative (starts with 0).
Proof:
And THEN you can read the proof in the notes.
You do it!

## Slide 6: Long Definition for Overflow of 2’s Complement Addition
Add two N-bit 2’s complement patterns.
A aN-2 … a0 (sign bit is A)
+ B bN-2 … b0 (sign bit is B)
S sN-2 … s0 (sign bit is S)
Claim: The addition overflows iff one of the following holds:
The two addends are non-negative, and the sum is negative.
The two addends are negative, and the sum is non-negative.
Notes: Explain both cases to make sure that students understand why they imply overflow. The harder part is showing the other direction: that overflow implies one of these two cases. That proof again is left to them (and is in the notes).

## Slide 7: Boolean Algebra Gives a More Concise Expression
That’s a lot of words!
Boolean algebra gives a more concise form:
OVERFLOW = [ (NOT A) AND (NOT B) AND C ] OR [ A AND B AND (NOT C) ]
(Remember: A, B, and C were the sign bits.)
But what do these operators (AND, OR, and NOT) mean?
Notes: Engineers hate words!

## Slide 8: Boolean Operators Were Invented in the mid-19th Century
Boolean operators were invented (by George Boole) to reason about logical propositions.
They originally operated on true/false values.
We use them with … that’s right, bits!
0 = false and 1 = true
Be careful not to confuse Boolean operators with English words. The meanings are not identical.

## Slide 9: We Use Only a Few Boolean Functions
AND: the ALL function returns 1 iff ALL inputs are 1 (otherwise 0)
OR: the ANY function returns 1 iff ANY input is 1 (otherwise 0)
NOT : logical complement (NOT 0) is 1; (NOT 1) is 0
XOR : the ODD function returns 1 iff an ODD number of inputs are 1 (otherwise 0)
Notes: Point out the difference between OR and “or.” For example, if a student came to my house, and I asked, “Would you like coffee, tea, milk, or orange juice?” I would consider it rude for the student to say, “Yes, all of them!” People sometimes say that English uses an exclusive or (exactly one of the answers), but XOR is not the same as English “or,” either (except for 2 inputs). The point: don’t try to apply English meanings.

## Slide 10: A Truth Table Fully Defines a Boolean Function
The drawing to the right is a truth table.
A truth table allows us to
  define a Boolean function C
  by listing the output value
  for all combinations of inputs (here A and B, in base 2 order).
Let’s write truth tables for our four Boolean functions.
A | B | C
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 11: AND: The ALL Function
Let’s start with AND.
AND can be written in several ways:
  AB
  A·B
  A×B
  A^B (math. conjunction)
A | B | A AND B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
0
1
A
B
AB
We usually use these.
Note flat input, rounded output.
Notes: Let the students fill in the table, top to bottom. Mention that we use the algebraic notation for multiplication for AND. The drawing is an “AND gate,” which we use to compose functions and design hardware.

## Slide 12: OR: The ANY Function
And now OR.
OR can also be written in other ways:
  A + B
  AB (math. disjunction)
A | B | A OR B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
1
We usually use this one.
Note rounded input, pointed output.
A
B
A+B
Notes: Let the students fill in the table, top to bottom. Mention that we use the algebraic notation for addition for OR. The drawing is an “OR gate.”

## Slide 13: NOT: Logical Complement
And now NOT.
NOT can also be written in other ways:
  A’
  A
   A (math. complement)
A | NOT A
0 | 
1 | 
1
0
We usually use these.
Note triangle and
inversion bubble.
A
A’
Notes: Let the students fill in the table, top to bottom. The drawing is an inverter, or a “NOT gate.” The bubble signifies the complement: without the bubble, it’s just a buffer (to amplify the signal / improve speed).

## Slide 14: XOR: The ODD Function
And, finally, XOR.
XOR is usually written this way: A  B
A | B | A XOR B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0
Note: like OR, but
double line for inputs.
A
B
AB
Notes: Let the students fill in the table, top to bottom. The drawing is an “XOR gate.” The inputs may or may not cross the first line and reach the second (they’ll see both variants—it doesn’t matter).

## Slide 15: Use Definitions to Generalize to More than Two Operands
Generalize to more operands using the definitions given:
  AND: ALL
  OR: ANY
  XOR: ODD
As an example, fill the truth table for a 3-input XOR.
A | B | C | ABC
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
1
0
1
1
0
1
0
Notes: Let the students fill in the table.

## Slide 16: Generalize to Sets of Bits by Pairing Bits
We can also generalize to sets of bits.
For example, if we have two N-bit patterns,
A=aN-1…a0 and B=bN-1…b0,
we can write
C = A AND B
To mean that
if C=cN-1…c0, ci = aibi for 0 ≤ i < N.
Notes: Bitwise operations are common in instruction set architectures, and students will make use of them in their first assembly programming assignments near the end of the course.

## Slide 17: Don’t Mix Algebras: Use AND/OR/NOT for Bitwise Logic
If A is a 2’s complement bit pattern, we might also write -A = (NOT A) + 1
Be careful about mixing
  algebraic notation for Boolean functions
  with arithmetic operations.
The “+” in the equation above means base 2 addition (and discarding any carry out), not OR.

## Slide 18: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Logical Completeness

## Slide 19: Can We Count Functions?
A question for you:
How many different Boolean functions exist for N bits of input?
How can we find the answer?
Start by thinking about small values of N.
For example, N=2. Given C = F(A,B), how many choices do we have for F?
Notes: Make sure that the students understand the general strategy of trying to solve small N and then generalizing the approach and/or using induction to solve the general problem.

## Slide 20: Two Bits of Input Can be Combined into 16 Functions
Write a truth table for C = F(A,B).
But instead of filling in values, call the outputs ci.
The four ci values uniquely specify F.
If we change any ci, we get a different function.
We thus have 2×2×2×2 = 24 choices for F.
A | B | C
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
c0
c1
c2
c3

## Slide 21: Three Bits of Input Can be Combined into 256 Functions
What about N=3: D = G(A,B,C)?
We can again write a truth table.
And call the outputs di.
Now we have 28 choices for G.
Notice that 28 = 2(23).
A | B | C | D
0 | 0 | 0 | d0
0 | 0 | 1 | d1
0 | 1 | 0 | d2
0 | 1 | 1 | d3
1 | 0 | 0 | d4
1 | 0 | 1 | d5
1 | 1 | 0 | d6
1 | 1 | 1 | d7

## Slide 22: N Bits of Input Can be Combined into Many Functions
Can we generalize to N bits?
Without drawing a truth table, please?
N bits means 2N rows in the truth table.
Thus we need 2N Boolean values (bits) to specify a function.
Thus 2(2N) possible functions on N bits.

## Slide 23: We Need More Functions!
So why did we teach you only four functions?
(AND, OR, NOT, and XOR)
Your homework for next time:
Write down and name all functions on 10 bits.
Include a truth table for each function!
Notes: Can’t guarantee that my colleagues won’t assign infinite homework. But don’t stress. First, if the homework is infinite, the curve will be gentle. And, second, many of them will actually use a curve!

## Slide 24: Alternate Homework: Understand Logical Completeness
Claim:
With enough 2-input AND, 2-input OR, and NOT functions, one can produce any function on any number of variables.
Believe me?
Proof: by construction
In other words, I’ll show you how to produce an arbitrary function on an arbitrary number of variables.
Notes: Students should only believe claims after they’ve been proven. Or, like Fermat, they can prove the theorem themselves and then check whether the professor got it right. They should know what “by construction” means for proofs.

## Slide 25: Compose Functions to Produce Functions on More Inputs
Let’s start the proof.
What does this circuit produce?
A 3-input AND!
What about this one?
A 4-input AND!
A
B
C
A
B
D
C
ABC
ABCD
Notes: Students should be able to give the answer before it is revealed (ask them).

## Slide 26: Use 2-Input Gates to Construct N-Input Gates
By induction, we build an N-input AND gate.
Base case (N=2): Use one 2-input AND.
N+1 case (given an N-input AND):
  Use one N-input AND
  and one 2-input AND
  to produce an (N+1)-input AND.
A0
AN
AN-1
…
A0 … AN-1
A0 … AN-1AN
Notes: Make sure that they remember and understand proof by induction.

## Slide 27: Comments on Functional Form and Practical Value
A couple of comments before we continue…
  Functional form of the inductive proof:
    base: AND2 (A, B) = AND2 (A, B)
    inductive step: ANDN+1 (A0, …, AN) = AND2 (ANDN (A0, …, AN-1), AN)
  This approach is an existence proof, not a practical way to build bigger gates.

## Slide 28: The Claim is Now Slightly Simpler
Claim:
With enough 2-input AND, 2-input OR, and NOT functions, I can produce any function on any number of variables.
(For OR functions, use the same approach as we did with AND functions, replacing AND with OR.)
Let’s first consider functions that
  produce an output of 1
  for exactly one combination of inputs (one row of the function’s truth table).

## Slide 29: One AND Suffices for Functions that Output One 1
The function Q(A,B,C) is an example of such a function.
When is Q=1?
Only when A=1 AND B=0 AND C=1.
Note that B=0 when (NOT B) = 1.
In other words, Q = AB’C.
A | B | C | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Let the students answer the question.

## Slide 30: Arbitrary Functions Require Only Two Steps
To produce an arbitrary function (which may produce the value 1 for more than one combination of inputs):
For each combination of inputs for which the function produces a 1, AND together the corresponding inputs or inverted inputs.*
OR together the results of all AND functions.
* The resulting AND is called a minterm on the input variables.

## Slide 31: A Sum-of-Products Can Express Any Function
The construction described results in a sum-of-products form because
  we produce each row of the truth table with an AND (product / multiplication notation)
  we produce the final function by ORing the ANDs (sum / addition notation).
The approach described is often inefficient, but it always works.

## Slide 32: {AND, OR, NOT} is Logically Complete
Definition: The set {AND, OR, NOT} is logically complete because, as we showed,
any Boolean logic function on any number of inputs can be produced using only AND, OR, and NOT.
To show that another set is logically complete
  You need not construct arbitrary functions.
  You need only show how to construct AND, OR, and NOT.

## Slide 33: Why Do You Care? Abstraction!
Imagine working on a new device technology.
  Maybe it’s based on DNA.
  Maybe it’s based on new semiconductors.
  Maybe it’s based on carbon nanotubes.
  Maybe you’re still finishing your degree?!
What do you need to be able to build in order to replace the current technology?
AND, OR, and NOT.
Other people can then build higher layers of abstraction!
Notes: Be sure to point out to students that we have active research programs in many areas that they can explore later.

## Slide 34: Example: 3-input XOR
Let’s build XOR as an example.
First, write the truth table.
What function produces this row?
And this row?
And this one?
And this one?
A | B | C | X
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
1
1
0
1
0
0
1
A’B’C
A’BC’
AB’C’
ABC
Notes: Let the students guide the process.

## Slide 35: 3-input XOR Expressed Using AND, OR, and NOT
Putting these four functions together, we obtain:
A XOR B XOR C = A’B’C + A’BC’ + AB’C’ + ABC
Now we are ready to begin building devices such as adders and comparators to manipulate our representations…