## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Fixed- and Floating-Point Representations

## Slide 2: In Binary, We Have A Binary Point
Let’s talk about representations.
In decimal, we have a decimal point.
3.1415...
In binary, we have a binary point.
11.001001…
tenths
hundredths
2-1’s place
2-2’s place
2-3’s place
Notes: After the decimal/binary point are place values with negative powers of 10/2, respectively.

## Slide 3: Fixed-Point Representations Support Fractions
If we need fractions,
  we can use a fixed-point representation
  in which some number of bits
  come after the binary point.
For example, with 32 bits:
Some signal processing and embedded processors use fixed-point representations.
integer part
(16 bits)
fractional part
(16 bits)
Notes: The position of the binary point in “fixed-point” can be tracked in hardware, software, or both. Much of the arithmetic hardware can be shared with unsigned / 2’s complement, too.

## Slide 4: What about Real Numbers?
A question for you:
Do we need anything else to support real numbers?
Note: Saying “yes” on the basis that there are uncountably many* real numbers is not a good answer. Integers are also infinite, and 2’s complement is sufficient for practical use.
* An infinite number for each integer.

## Slide 5: Isn’t Fixed-Point Good Enough?
Let’s do a calculation.
32-bit 2’s complement has what range?
That’s right: [-2,147,483,648, 2,147,483,647].
You DID all know that, right?
I didn’t. I usually write [-231, 231 – 1].
Let’s write banking software to count pennies.
2,147,483,647 pennies is $21,474,836.47.
Anyone here have more? If not, we’re done.
If so, use 64-bit. You don’t have that much!

## Slide 6: Anyone Here Taking Chemistry?
But maybe you want to do your Chemistry homework?
You may need Avogadro’s number.
Anyone remember it?
Sure. No problem.
103 is around 210, so 80 bits should work.
Who can tell me Avogadro’s number to 80 bits (the first 24 decimal digits will do)?
6.022 × 1023 / mol
Notes: Tease them about not knowing it. Tell them you’ll tell their Chemistry professor.

## Slide 7: Wikipedia May Not Help as Much as You Think!
Last I checked (July 2016!), the best known experimental value was
6.022140858 × 1023 / mol
That’s only 10 digits.
So you have some serious Chemistry research to get done for your next homework!
Good luck!
Maybe we can just be close?

## Slide 8: What about Physics?
Some have Quantum Mechanics homework?
Your computer will need Planck’s constant.
What is it again?
Ok. Another 90 bits after the binary point.
170 bits total.
Don’t forget to find another 90 bits (27 more decimal digits) for Avogadro.
*Use ergs, not Joules; we’ll need fewer bits!
6.626 × 10-27 erg-sec*

## Slide 9: We Need More Dynamic Range, Not More Precision
Do we really need 170 bits of precision?
Do we really need to specify the first 51 significant figures for Avogadro’s number?
Of course not!
But we do need 170 bits of range.
We need to be able to express both tiny numbers and huge numbers.

## Slide 10: Develop a Representation Based on Scientific Notation
Let’s borrow another representation from humans: scientific notation.
+ 6.022 × 10 23
The human representation has three parts.
sign
mantissa/significant figures (precision)
exponent

## Slide 11: Modern Computers Use Standard Floating-Point
Modern digital systems implement the IEEE 754 standard for floating-point.
A single-precision floating-point number consists of 32 bits:
What value does a bit pattern represent?
First, let me ask you a question…
sign
(1 bit)
exponent
(8 bits)
mantissa
(23 bits)
Notes: Courtesy of Velvel Kahan.

## Slide 12: What Values Can a Leading Digit Take?
A question for you:
In the canonical form of scientific notation, what are the possible values of the leading digit?
- 4.123 × 1045
Any digit?
1-9 (not 0). Change exponent as needed.
This one
0-4?
1-7?

## Slide 13: What Values Can a Leading Digit Take?
Another question for you:
Same question, but now in binary.
1 (not 0). Change exponent as needed.
And one more:
How many bits do we need to store one possible answer?
The leading 1 is implicit in binary (0 bits)!

## Slide 14: How to Calculate the Value of a Floating-Point Bit Pattern
The value represented by an IEEE single-precision floating-point bit pattern is…
(-1)sign 1.mantissa × 2(exponent – 127)
Convert the exponent to decimal as if it were unsigned before subtracting 127.
sign
(1 bit)
exponent
(8 bits)
mantissa
(23 bits)
Notes: Be sure to point out the implicit “1” at the first digit of the scientific notation (which is in binary).

## Slide 15: Except that Exponents 0 and 255 have Special Meanings
That’s almost correct. But exponents 0 and 255 have special meanings:
  255 can mean infinity or not-a-number (NaN).
  0 is a denormalized number: the leading implicit “1” is replaced with “0” (with power 2-126), allowing the representation to capture numbers closer to 0.
Except for the fact that the bit pattern of all 0s means 0, these aspects are beyond the scope of our class.
Notes: This slide is here for students to read, but there’s no need to dwell on it in a lecture. They just need to be aware. There are actually two bit patterns for 0, but making 0 the same as its integer representation was deliberate.

## Slide 16: Exponent 255 is Used for Infinity and NaN
Exponent 255
  Mantissa 0
    Sign 0: Positive infinity
    Sign 1: Negative infinity
  Non-zero mantissa: NaN (Not a Number)
These special values allow the representation to have ‘correct’ answers to some problems (such as 42.0 / 0.0) and to silently track the impact of missing values and incorrect computation (such as Infinity * 0).
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Notes: Well, it seems that I have extra time, so I can talk about looking at data dependences with NaN, generating NaNs accidentally, and so forth.

## Slide 17: Denormalization Allows Numbers Closer to 0 (and 0)
Without denormalized numbers, we have (shown with a 3-bit mantissa)…
Denormalization puts these patterns closer to 0 and gives two patterns for 0:
2-127
2-126
-2-127
-2-126
(0)
2-127
2-126
-2-127
-2-126
0
(two patterns)
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Notes: I had extra time in F16, so I’m adding a couple of extra material slides.

## Slide 18: Converting to a Floating-Point Bit Pattern
Conversion from decimal to IEEE floating-point is not too hard:
Convert to binary.
Change to scientific notation (in binary).
Encode each of the three parts.

## Slide 19: Use a Polynomial to Convert a Fraction to Binary
To convert a fraction F to binary, remember that a fraction also corresponds to a polynomial:
F = a-12-1 + a-22-2 + a-32-3 + a-42-4 + …
If we multiply both sides by 2
  the left side can only be ≥ 1
  if a-1 = 1
We can then subtract a-1 from both sides
and repeat to get a-2, a-3, a-4, and so forth.

## Slide 20: Example of Finding a Floating-Point Bit Pattern
For example, let’s say that we want to find the bit pattern for 5.046875.
We first write 5 in binary: 101.
Now we need to convert the fraction
F = 0.046875.
0.046875 × 2 = 0.09375 (< 1, so a-1 = 0)
0.09375 – 0 = 0.09375

## Slide 21: Example of Finding a Floating-Point Bit Pattern
Start with 0.09375.
0.09375 × 2 = 0.1875 (< 1, so a-2 = 0)
0.1875 – 0 = 0.1875
0.1875 × 2 = 0.375 (< 1, so a-3 = 0)
0.375 – 0 = 0.375
0.375 × 2 = 0.75 (< 1, so a-4 = 0)
0.75 – 0 = 0.75

## Slide 22: Example of Finding a Floating-Point Bit Pattern
Start with 0.75.
0.75 × 2 = 1.5 (so a-5 = 1)
1.5 – 1 = 0.5
0.5 × 2 = 1 (so a-6 = 1)
1 – 1 = 0 (done)
Putting the bits together, we find
F = 0.04687510 = 0.0000112

## Slide 23: Example of Finding a Floating-Point Bit Pattern
Now we have converted to binary:
5.04687510 = 101.0000112
In binary scientific notation, we have
+ 1.01000011 × 22
And, in single-precision floating point,
  the sign bit is 0,
  the exponent is 2+127 = 129 = 10000001,
  and the mantissa is 01000011… (no leading 1, and 15 more 0s afterward).

## Slide 24: Tricky Questions about Floating-Point
A question for you:
What is 2-30 + (1 – 1)?
Quite tricky, I know. But yes, it’s 2-30.
Another question for you:
What is (2-30 + 1) – 1?
That’s right. It’s 0.
At least it is with floating-point.

## Slide 25: Floating-Point is Not Associative
Why?
Our first sum was (2-30 + 1).
To hold the integer 1, the bit pattern’s exponent must be 20.
But, the mantissa for single-precision floating point has only 23 bits.
And thus represents powers down to 2-23.
The 2-30 term is lost, giving (2-30 + 1) = 1.
So 2-30 + (1 – 1) ≠ (2-30 + 1) – 1.
Notes: Students should be encouraged to take a class in numerical analysis if they are interested in understanding how to handle such problems. The problems are quite subtle and difficult and should not be underestimated. Many capable scientists have been fooled by numerical errors in their computer simulations.

## Slide 26: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Hexadecimal, Text, and Terminology for Representations

## Slide 27: Some Sugar-Coating for Humans
Bits are a bit of a pain. For example, try to memorize this pattern:
00010011010101100111
But computers always use bits!
Humans, on the other hand,
  can use base 16,
  usually called hexadecimal, or hex,
  to make dealing with bit patterns easier.
Have you memorized the pattern?
Hurry up!

## Slide 28: Convert Hex to/from Binary in Groups of 4 Bits
Hex includes A through F to get 16 digits:
0 1 2 3 4 5 6 7 8 9 A B C D E F
16 = 24, so each hex digit represents four bits.
Remember:
  Use of hex only serves to help humans write and remember bits!
  Digital systems just use bits.

## Slide 29: Time for a Pop Quiz!
Ok, what is the bit pattern?
Seriously?
Maybe you remember a few of them?
What if this is were an exam question?
Sigh.
Ok, it was 00010011010101100111.
In hex, that’s x13567 (P&P/LC-3 hex notation—otherwise, 13567 is probably decimal!).
Can you remember that? Please?

## Slide 30: Text was Historically Represented with ASCII
How do we represent text?
One early system was the American Standard Code for Information Interchange (ASCII).
ASCII is a 7-bit code representing
  English letters A-Z in both cases
  (Arabic) digits 0-9
  Punctuation
  Some special symbols ($, #, %, and so on)
  Control characters for terminals

## Slide 31: A Few Other Text Representations
The ubiquity of the 8-bit byte gave rise to “extended” (8-bit) versions of ASCII.
These were not standardized.*
What about other languages?
  UIUC (NCSA) invented the browser in 1993
  and the Internet received global attention.
  Unicode (16-bit) includes characters for many other languages.
* There are 8-bit standard encodings for text today, but our goal is not an exhaustive list.
Notes: As of 2016, MIT’s media engine has expanded its claims and are pushing the idea that Berners-Lee invented the browser. NCSA was the first to integrate text and images and links. Other people had done text and links (before Berners-Lee), and had done cross-domain text (Gopher), hypertext within organizations, etc. Berners-Lee suggested inter-domain hypertext with search, and as part of the project, they made up a markup language (SGML, precursor of HTML).

## Slide 32: Terminology: Representations vs. Data Types
We will try to differentiate between
  representation: ways of encoding specific types of information into bit patterns
  data type: a specific number of bits encoded with a specific representation
Examples of data types include: 8-bit unsigned, 16-bit 2’s complement, IEEE 754 single-precision floating point
High-level languages such as C associate values with data types.
Notes: The last point is for the near future—usually the following week for the students.

## Slide 33: Illustration of a Representation Taxonomy
data types
bits
things being
represented
IEEE 754
single-prec.
non-negative
integers
integers
text
real
numbers
vegetables
unsigned
16-bit unsigned
signed- magnitude
2’s com-
plement
32-bit 2’s com-
plement
64-bit 2’s com-
plement
Unicode (16-bit)
ASCII
7-bit
ASCII
floating- point
fixed- point
representations
Notes: Subdivide first by the type of thing being represented, then by representation, and finally by data type. Point out that this taxonomy is necessarily partial: first, there are infinite data types corresponding to unsigned, 2’s complement, and so forth; and, second, we leave out many others for space reasons.

## Slide 34: Remember: Computers Do Not “Understand” Bits
Human text usually in ASCII or Unicode
  human-readable files
  your typing
  text printed for you to read
Computer do not “understand” what the bits mean.

## Slide 35: Computers Always Do What They’re Told
For example, what does a computer do if someone tells it …
  to add the ASCII character “3” (0110011)
  to the ASCII character “2” (0110010)?
The computer adds them!
Using an adder…
Natural log just got simpler!
1
1
0
1
0
1
1
1
1
0
0110011 (“3”)
+ 0110010 (“2”)
(“e”)

## Slide 36: Computers Require Explicit Instructions
To get the “right” answer, someone (a human) must tell the computer
  to convert the ASCII to unsigned or 2’s complement
  to add the converted values, and
  to convert the sum back to ASCII!

## Slide 37: Second-Chance Pop Quiz!
Ok, what is the number in hex?
x13567
Memorizing numbers is not a learning objective in ECE120.
But you probably get the point of the exercise.
Hex makes it easier to deal with bits.
(You may find hex harder to use for arithmetic and logic calculations, though.)