## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Two-Level Logic

## Slide 2: SOP Form Gives Good Performance
As you know, one can use a K-map to obtain an SOP form.
If one chooses
  a minimal number of loops of maximal size
  the resulting SOP form has optimal area*
But what about speed?
The speed of an SOP form is typically optimal.
*See caveats in slides on K-maps.

## Slide 3: The Best Case is One Gate Delay*
Recall our delay heuristic: the number of gate delays from any input.
Let’s assume that complemented literals are available with no delay.
What can we express with one gate delay in CMOS?
Only NAND and NOR (NOT is a 1-input NAND/NOR).
*Ignoring the functions 0 and 1 and functions consisting of a single literal, all of which have zero gate delays.
Notes: Ask them.

## Slide 4: K-Maps Can Identify Single-Gate Functions
A single NAND is an SOP expression.*
So is a single NOR.
An expression using a single gate is also optimal by our area heuristic.
So if a function can be built with a single gate, the K-map will give us that expression.
*And a POS expression.
Notes: Students need to understand DeMorgan’s Laws to agree with the first claim (about a NAND being an SOP expression). If they get confused, tell them to wait a few minutes, then come back to it.

## Slide 5: Is Counting AND/OR Gates Realistic?
Most functions cannot be expressed as a single NAND/NOR gate.
So how fast is an SOP expression?
Two gate delays.
AND, followed by OR.
But in CMOS, we only have NAND and NOR.
How many gate delays do we get if we only use NAND/NOR?
Notes: Ask students.

## Slide 6: Let’s Introduce Some Algebra
A little Boolean algebra will help us:
DeMorgan’s Laws
(AB)’ = A’ + B’ (A+B)’ = A’B’
Want a proof? Use a truth table (4 lines each).
They also generalize to more than two inputs.
For example,
(ABC)’ = A’ + B’ + C’ (A+B+C)’ = A’B’C’

## Slide 7: DeMorgan’s Laws Relate NAND/NOR to AND/OR
What do DeMorgan’s Laws mean?
Here’s one way to think about them:
  (AB)’ = A’ + B’ NAND is the same as OR on the complements of the inputs.
  (A+B)’ = A’B’ NOR is the same as AND on the complements of the inputs.

## Slide 8: A Graphical Representation Can Be Useful, Too
Let’s also think about them graphically.
Complement both sides first, so we have…
AB = (A’ + B’)’ A+B = (A’B’)’
and now we can draw gates…
A
B
A
B
A
B
A
B

## Slide 9: How Do We Draw an SOP Form? AND, then OR
What were we talking about?
Ah, speed of SOP forms.
SOP is AND followed by OR.
Something like this…
(with some number of AND gates, each with some number of inputs)
Notes: Remind the students that they should always keep the main topic in mind. It’s easy to get distracted sometimes…

## Slide 10: Apply DeMorgan’s Laws Graphically
Use DeMorgan’s law on the OR gate.
Replace it with a NAND with inverted inputs.

## Slide 11: Apply DeMorgan’s Laws Graphically
Use DeMorgan’s law on the OR gate.
Replace it with a NAND with inverted inputs.
Remember that the input bubbles mean inverters (NOT).
Now slide them down the wires to the left until they sit in front of the ANDs.

## Slide 12: Apply DeMorgan’s Laws Graphically
Use DeMorgan’s law on the OR gate.
Replace it with a NAND with inverted inputs.
Remember that the input bubbles mean inverters (NOT).
Now slide them down the wires to the left until they sit in front of the ANDs.

## Slide 13: SOP Form Speed is Two Gate Delays
We didn’t change the function of the circuit.
But now all of the gates are NAND gates.
So we can build any SOP function using two levels of NAND.
And the speed? Two gate delays.

## Slide 14: SOP and POS Forms Give Us Two-Level Logic
We can use two levels of NANDs to build any SOP expression.
We refer to this approach as two-level logic.
For a POS expression
  one can do exactly the same thing
  replacing OR followed by AND
  with NOR followed by NOR.
So any POS expression also requires two gate delays (again, assuming that complemented inputs are free).

## Slide 15: Use a K-Map to Find POS Expressions
But how can we find a POS form?
Again, use a K-map.
Given a function F, draw a K-map for F’.
Use K-map to find an SOP form for F’.
Complement the result to find F
  and apply DeMorgan’s laws a few times,
  complement of SOP form is POS form.

## Slide 16: In Practice, Form Loops Around 0s to Find POS
In practice, just circle 0s instead of 1s.
Recall that a box in a K-map
  when filled with a 1
  corresponds to a minterm.
The same box
  when filled with a 0
  corresponds to a maxterm
  an expression that produces exactly one 0 row in its truth table.

## Slide 17: Complement Literals When Reading POS Factors
But be careful: the maxterm has all variables complemented relative to the minterm.
For example,
  a box corresponding to minterm ABC’ (equal to 1 when A=1 and B=1 and C=0)
  corresponds to maxterm A’ + B’ + C (equal to 0 when A=1 and B=1 and C=0)

## Slide 18: SOP and POS Forms Give Us Two-Level Logic
To find a POS form that has optimal area (among POS forms),
  follow the same approach as before,
  but instead of drawing loops around 1s,
  draw loops around 0s.
Again, do not forget to complement the literals relative to their form for implicants!
(And write each loop as a sum, not as a product.)

## Slide 19: Which Form is Better? Solve Both and Compare
Which gives better area, SOP or POS?
That depends on the function.
Solve both ways and compare.
You will have some experience finding POS forms in discussion section.
You can also use the online tool, but the exercises are not as direct as for SOP.
Notes: Yikes. No loop mark and check for POS in the tool. Should I write it? Or is it enough for them to learn SOP and understand POS via duality?

## Slide 20: Summary of 2-level Design
Every Boolean function can be expressed as
Minimal SOP (or POS) expression
And can be implemented as
AND-to-OR (or OR-to-AND) two-level network
Or as
NAND-to-NAND (or NOR-to-NOR) two-level network

## Slide 21: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Pareto Optimization*
Notes: This material is NOT REQUIRED LEARNING, but is something that all of our students should see early in their careers, so we just spend a little time showing them the kind of thing that they will need to deal with every day as engineers. The main idea is to use mathematical dominance to avoid making decisions about tradeoffs before it’s necessary. It’s also nice if they remember that they heard about Pareto curves/surfaces at some point in their education.

## Slide 22: What’s Best When We Have Several Metrics?
As engineers, you will rarely have the luxury of a single metric.
How does one choose between metrics?
Imagine the following …
  You are working as an intern
  designing hardware to execute DNNs (deep neural networks, which may be useful in a variety of tasks).
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 23: Example: Compare Designs Based On Area and Delay
Building on your ECE120 knowledge, you have two metrics.
  Area, which you have normalized from 1 to 100.
  Delay, which you have also normalized from 1 to 100.
In both metrics, smaller is better.
For a design X, A(X) is the area, and D(X) is the delay.
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 24: Which Metric is More Important?
Now imagine that you have two designs, X and Y.
How do you choose between them?
Which is more important, area or delay?
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 25: The Answer Depends on How the Design is Used
The answer depends on the context in which your design is used
  datacenter
  laptop
  mobile phone
  car or other vehicle
  space probe
  children’s toy
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 26: One Option is to Combine Metrics Numerically
How do you make a choice?
One option: linearize. Pick some weights
  actually, one weight W is enough
  W is the relative importance of delay compared to area
Then
  for each design X
  calculate M(X) = A(X) + W D(X)
Choose the design with the smallest M(X).
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Notes: Any mathematical function is possible, linear or non-linear or even combinatoric. Stress that picking such a function is making a choice about relative importance of metrics, regardless of how the function is formulated.

## Slide 27: Relative Importance is Not Easy to Choose in Practice
But how do you pick W?
What if you need designs for ALL of those applications?
As an engineer, you may not be in a position to know the right weights!
So what can you do if you don’t know the relative importance of the metrics?
For two designs, probably just report both to your manager.
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 28: Remember Dilbert? Oxygen is Good.
What if you have created 10,000 designs?
  Not by hand, but by using parameters.
  For example, does your design provide hardware for 8-bit, 16-bit, 32-bit, or 64-bit addition?
  Do you report all 10,000 to your manager?
  Probably not if you want a job offer.
  But what can you do?
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 29: A Design that is Worse in All Metrics is Pareto-Dominated
Pick two designs X and Y.
What if A(X) < A(Y) AND D(X) < D(Y)?
Remember that smaller is better for both area and delay.
In such a case, do you need to report Y?
No! X is better in both metrics.
We say that design Y is Pareto-dominated by design X.
If there were N metrics, Y must be worse than some X in ALL metrics to be Pareto-dominated.
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 30: Eliminate Designs that are Pareto-Dominated by Others
You can use the idea of Pareto domination to eliminate designs.
Any design that is Pareto-dominated by any other design can be discarded.
Only designs that may be better in some context remain.
The remaining designs form a Pareto curve (a Pareto surface for more than two metrics).
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

## Slide 31: A Graph Illustrates Pareto-Dominance (Small is Good)
dominated by point P
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Chart: All Possible Designs
| 40 | 20 | 30 | 17 | 65 | 24 | 10 | 55 | 93 | 40 | 30 | 29 | 44 | 60 | 45 | 25 | 65 | 75 | 80 | 85 | 99 | 90 | 75 | 48 | 52
Y-Values | 18 | 40 | 22 | 80 | 12 | 36 | 94 | 17 | 8 | 70 | 35 | 80 | 74 | 40 | 40 | 59 | 80 | 20 | 65 | 35 | 99 | 70 | 93 | 83 | 55
P

## Slide 32: A Pareto Curve (after Discarding Dominated Points)
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Chart: Pareto Curve
| 40 | 20 | 30 | 17 | 65 | 24 | 10 | 55 | 93
Y-Values | 18 | 40 | 22 | 80 | 12 | 36 | 94 | 17 | 8
P

## Slide 33: Use of Pareto Curves/Surfaces is Common
In many hardware design environments, engineers run design-space exploration tasks (on computers, of course!):
  Given a set of parameters for a design
  Generate hardware for each possible combination of parameters
  Then use Pareto dominance to trim the results down
  And show the engineer the Pareto surface of area, delay, and power consumption.
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *
Notes: Brief example and reference to Neal Crago’s thesis appear in the notes Section 2.1.6 (*’d like this entire deck of slides).

## Slide 34: Want to Learn More about Optimization?
Take ECE490 some day.
Combines theory and practice:
  optimization algorithms,
  Implementations,
  use of libraries to solve problems.
* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *