## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
A Power-of-Two Checker

## Slide 2: Powers of Two are Easy to Spot in Binary
Let’s do another bit-sliced design.
Can we check whether an unsigned number represents a power of two?
What does a power of two look like in bits?
For 5-bit unsigned, the powers of 2 are...
00001, 00010, 00100, 01000, 10000
A power of two has exactly one 1 bit (with place value 2N for some N, of course!).

## Slide 3: The Answers are Not Always Enough
So our design will answer the following: Is A = aN-1aN-2…a1a0 a power of two?
How many answers are possible?
Two: Yes, and No.
A trick question:
How many bits do we need to pass between slices?
That’s right: TWO bits.

## Slide 4: What Extra Information Do We Need?
Why not just one? An answer only needs 1 bit!
Say that we pass bits from right to left.
If the bits aN-2…a1a0 represent a power of two, is aN-1aN-2…a1a0 be a power of two?
What if aN-2…a1a0 does not represent a power of two?
In that case, we can’t tell whether aN-1aN-2…a1a0 is a power of two or not!
What else do we need to know?
Iff aN-1 = 0.

## Slide 5: For Inductive Step, We Must Know Whether all Bits are 0
Imagine that we have completed N-1 bits.
Under what conditions can number A be a power of two?
  aN-1 = 1 and the rest is all 0s, or
  aN-1 = 0 and the rest is a power of two.
For #2, we need to know whether the rest of the bits form a power of two.
But for #1, we also need to know whether the rest of the bits are all 0.

## Slide 6: There are Three Possible Messages between Bit Slices
The “yes” cases for #1 and #2 do not overlap: all 0 bits is not a power of two.
The “no” cases need not be further separated:
  all 0s means no 1 bits
  a power of two means one 1 bit
  more than one 1 bit means “no” to both questions
That’s all we need to know. Three possible messages between slices, so two bits.

## Slide 7: We Need a Representation for Answers
I’ll use the following representation.
Others may be better.
C1 | C0 | meaning
0 | 0 | no 1 bits
0 | 1 | one 1 bit
1 | 0 | not used
1 | 1 | more than one 1 bit

## Slide 8: We Need a Representation for Answers
Let’s build a slice that operates on two bits of A.
In the bit slice, we call them A and B.
Inputs from the previous bit slice are C1 and C0.
Outputs to the next bit slice are Z1 and Z0.
Direction of our operation doesn’t matter. Either will do.

## Slide 9: Two Zeroes Do Not Change the Result
Let’s fill in a truth table.
We’ll start with the case of A = 0 and B = 0.
A | B | C1 | C0 | meaning | Z1 | Z0 | meaning
0 | 0 | 0 | 0 | no 1s |  |  | 
0 | 0 | 0 | 1 | one 1 |  |  | 
0 | 0 | 1 | 0 | ??? |  |  | 
0 | 0 | 1 | 1 | >one 1 |  |  | 
no 1s
>one 1
one 1
don’t care
0
0
0
1
x
x
1
1
Notes: Representation is replicated in the incoming bits, so you shouldn’t need to flip back.

## Slide 10: One 1 Input Increments the Count of 1 Bits
Now consider A = 0 and B = 1.
A | B | C1 | C0 | meaning | Z1 | Z0 | meaning
0 | 1 | 0 | 0 | no 1s |  |  | 
0 | 1 | 0 | 1 | one 1 |  |  | 
0 | 1 | 1 | 0 | ??? |  |  | 
0 | 1 | 1 | 1 | >one 1 |  |  | 
one 1
>one 1
>one 1
don’t care
0
1
1
1
x
x
1
1
Notes: Representation is replicated in the incoming bits, so you shouldn’t need to flip back.

## Slide 11: One 1 Input Increments the Count of 1 Bits
The case for A = 1 and B = 0 is the same.
A | B | C1 | C0 | meaning | Z1 | Z0 | meaning
1 | 0 | 0 | 0 | no 1s |  |  | 
1 | 0 | 0 | 1 | one 1 |  |  | 
1 | 0 | 1 | 0 | ??? |  |  | 
1 | 0 | 1 | 1 | >one 1 |  |  | 
one 1
>one 1
>one 1
don’t care
0
1
1
1
x
x
1
1
Notes: Representation is replicated in the incoming bits, so you shouldn’t need to flip back.

## Slide 12: Two 1s in the Number Rules Out Powers of Two
Finally, consider A = 1 and B = 1.
A | B | C1 | C0 | meaning | Z1 | Z0 | meaning
1 | 1 | 0 | 0 | no 1s |  |  | 
1 | 1 | 0 | 1 | one 1 |  |  | 
1 | 1 | 1 | 0 | ??? |  |  | 
1 | 1 | 1 | 1 | >one 1 |  |  | 
>one 1
>one 1
>one 1
don’t care
1
1
1
1
x
x
1
1
Notes: Representation is replicated in the incoming bits, so you shouldn’t need to flip back.

## Slide 13: We Solve Z1 as a POS Expression
Let’s use a K-map to solve Z1. POS looks good.
What are the loops?
(C1 + A + B)
(C0 + A)
(C0 + B)
So Z1 = (C1 + A + B) (C0 + A)(C0 + B)
Z1 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
C1C0 | 00 | 0 | 0 | 1 | 0
 | 01 | 0 | 1 | 1 | 1
 | 11 | 1 | 1 | 1 | 1
 | 10 | x | x | x | x

## Slide 14: We Solve Z0 as an SOP Expression
Now let’s solve Z0. SOP and POS are the same.
What are the loops for SOP?
C0
A
B
So Z0 = (C0 + A + B)
Z0 |  | AB |  |  | 
 |  | 00 | 01 | 11 | 10
C1C0 | 00 | 0 | 1 | 1 | 1
 | 01 | 1 | 1 | 1 | 1
 | 11 | 1 | 1 | 1 | 1
 | 10 | x | x | x | x

## Slide 15: We Can Reuse Some Factors with Algebra
Notice that we can reuse factors from Z1 to calculate Z0:
Z1 = (C1 + A + B)(C0 + A)(C0 + B)
Z0 = (C0 + A + B) = (C0 + A) + (C0 + B)
Let’s draw the bit slice, then analyze its area and delay.

## Slide 16: Area is 6N, and Delay is N Gate Delays for N Bits
Here is an implementation of the bit slice using NAND and NOR. Let’s find area.
How many literals?
How many operations?
And delay?
2 on all paths.
So N gate delays for N bits.
C0
B
C0
A
C1
A
B
Z1
Z0
7
5 (4 NOR, 1 NAND)
Notes: Note that area of 12 handles 2 bits, so overall area is 6N. Overall delay is N because 2 gate delays handles 2 bits.

## Slide 17: Need One More Gate Delay to Get the Answer
But we don’t get an answer!
Our N-bit checker,
  composed of N/2 bit slices,
  produces only a “count” of 1 bits (0, 1, or “many”).
We want yes (P = 1) or no (P = 0)!
Looking at the representation, the fastest solution is to add an XOR gate at the end.
P = Z1  Z0 from the last bit slice.
So delay is actually N + 1 gate delays.

## Slide 18: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Building with Abstraction and a First Example

## Slide 19: Optimization at the Level of Gates is Always Possible
One can always solve a problem by
  developing complete Boolean expressions,
  solving for “good” forms with K-maps (or algebra, with more variables),
  implementing the resulting equations,
  tuning logic to reduce gate sizes (number of inputs) and fanout (the number of gates using a single gate’s output).
You can now perform such a process.
Notes: Point out that students (1) don’t have a lot of experience with the process yet, and (2) don’t have the details of particular semiconductor processes with regard to how many inputs or fanouts are “good.” But that’s ok—those things they can look up and/or learn over time. The main point is that they understand the tradeoff between human time and optimization. (Next slide…)

## Slide 20: But Optimization at Gate Level is Rarely Needed
Such detail is rarely needed for a satisfactory solution.
Instead, humans can
  use abstraction and build with components such as adders and comparators, or
  use extra levels of logic to describe functions more intuitively.
Computer-aided design (CAD) tools
  can help with low-level optimizations.
  In many cases, CAD tools can do better than humans because they explore more options.

## Slide 21: Tradeoffs are Always Made in Some Context
Context is important!
If a mechanical engineer produces a 0.5% boost in efficiency for internal combustion engines sized for automobiles, that engineer will probably win a major prize.
In our field, engineers spend a lot of time
  improving the designs of arithmetic units and memory, and
  improving CAD tools’ ability to optimize.

## Slide 22: But Optimization at Gate Level is Rarely Needed
“Premature optimization is the root of all evil.” – Sir C.A.R. “Tony” Hoare
Don’t spend time optimizing
  something that is likely to change, nor
  something that does not contribute much to the overall system goodness (any metric).
The flip side:
  don’t ignore scaling issues when choosing algorithms, and
  don’t design in a way that prohibits/inhibits optimization.
Notes: Students will need examples to help them understand. With scaling, one can use the example of returning the first midterm by walking around the room with each exam, asking each student in turn (even ones that have already gotten theirs back!), “Is your name X?” Total time: N^2. For prohibiting optimization, perhaps mention a company (not by name?) that uses non-standard interfaces for standard functions (such as USB). They do it to create an artificial monopoly so that they can charge higher prices, but they can only do so because the non-standard interfaces prevent/discourage people from providing better (cheaper, faster, lower-power) replacement parts.

## Slide 23: First Example: Subtraction
Let’s start with something simple.
Let’s build a subtractor.
How do we subtract as humans?

## Slide 24: Example: Subtraction of 5-Digit Numbers
Let’s do an example with 5-digit numbers
12345
- 871
Negate by finding
the “9’s complement”
and adding 1.
Notes: Just like you learned in elementary school!

## Slide 25: Example: Subtraction of 5-Digit Numbers
Let’s do an example with 5-digit numbers
12345
+ 99129
Good, we got the right answer (12345 – 871 = 11474)!
7
4
1
1
1
4
1
1
We have no
space for
that digit!

## Slide 26: Use an Adder to Implement a Subtractor
Ok, maybe your elementary school taught subtraction a different way.
But you probably did use that approach in your ECE120 homework to subtract unsigned and 2’s complement values.
A – B = A + (NOT B) + 1
(where “NOT” applies to all bits of B)
Instead of mimicking the human subtraction process, let’s use an adder to implement a subtractor…

## Slide 27: Use an Adder to Implement a Subtractor
Take a look at the design to the right.
The core is an N-bit adder.
We want to calculate the difference D = A – B.
We modify the inputs slightly to perform the subtraction.

## Slide 28: Convert B to its 1’s Complement
The input A is unchanged.
The input B is transformed to its 1’s complement.
How do we implement 1’s complement?
N inverters!

## Slide 29: With Cin = 1, the Adder Produces A - B
Finally, the Cin input is set to 1.
So what does the adder calculate?
A + (NOT B) + 1
which is A – B, as desired.

## Slide 30: Calculate D to Understand the Carry Out Signal
What does the carry out Cout mean?
Remember that the 1’s complement is (2N – 1) – B.
So we obtain D = A + (2N – 1) – B + 1 = A – B + 2N

## Slide 31: Carry Out Signal (Opposite Sense) Still Means Overflow
So D = A – B + 2N.
But Cout is the 2N term from the adder.
Thus
  Cout = 1 means A ≥ B
  Cout = 0 means A < B
So for unsigned subtraction Cout = 0 indicates overflow!

## Slide 32: Use a Control Signal to Select between Operations
What if we want a device that does both addition and subtraction?
We need a way to choose the operation.
Add a control signal S
  S = 0: addition
  S = 1: subtraction
And then modify the adder inputs with S
  A …
  B …
  Cin …
unmodified
B XOR S (bitwise)
S
Notes: Let the students answer. Be sure that they understand the modifications. Consider both the S=0 and S=1 cases at the end (walk through the different inputs).

## Slide 33: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Checking for Upper-Case Characters

## Slide 34: Task: Checking for an Upper-Case Letter
Let’s design logic to check whether an ASCII character is an upper-case letter.
In ASCII, 'A' is 1000001 (0x41), and 'Z' is 1011010 (0x5A).
Let’s say that the ASCII character is in C = C6C5C4C3C2C1C0.
How can we check whether C represents an upper-case letter?

## Slide 35: We Will Need a BIG Truth Table!
Should we write a truth table for U(C)?
Can we skip to the ones that matter?
C6 | C5 | C4 | C3 | C2 | C1 | C0 | U(C)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 0 | 0 | 0 | 1 | 
0 | 0 | 0 | 0 | 0 | 1 | 0 | 
0 | 0 | 0 | 0 | 0 | 1 | 1 | 
0 | 0 | 0 | 0 | 1 | 0 | 0 | 
0 | 0 | 0 | 0 | 1 | 0 | 1 | 
0 | 0 | 0 | 0 | 1 | 1 | 0 | 
0 | 0 | 0 | 0 | 1 | 1 | 1 | 
0
0
0
0
0
0
0
0
Notes: See if the students will let you fill it in… with their help, of course!

## Slide 36: Let’s Break the Truth Table into Eight Pieces
Can we break the truth table into pieces?
For example, let’s break the truth table
  into eight truth tables
  of 16 rows each.
Each piece represents one value of C6C5C4.
We can solve each piece with a K-map on C3C2C1C0.

## Slide 37: Some Functions are Quite Simple
Or maybe we don’t need a K-map for some.
Remember that 'A' is 1000001 (0x41), and 'Z' is 1011010 (0x5A).
Think about the table for C6C5C4 = 000?*
What is the function of C3C2C1C0?
(In other words, no ASCII character with C6C5C4 = 000 is an upper-case letter.)
* This notation means C6 = 0 AND C5 = 0 AND C4 = 0.
0

## Slide 38: Only Two of Our Functions are Not the 0 Function
For reference: 'A' is 1000001 (0x41), and 'Z' is 1011010 (0x5A).
Which of our eight functions are not the 0 function?
C6C5C4 = 100
C6C5C4 = 101
Let’s solve K-maps for these two.
Let’s call the function T4.
Let’s call the function T5.
Notes: Let the students answer. The relevant ASCII mapping is on the slide.

## Slide 39: Solve T4 Using a Single Loop
Let’s solve T4. Should we use SOP or POS?
T4 is a maxterm!
T4 = (C3 + C2 + C1 + C0)
T4 |  | C3C2 |  |  | 
 |  | 00 | 01 | 11 | 10
C1C0 | 00 | 0 | 1 | 1 | 1
 | 01 | 1 | 1 | 1 | 1
 | 11 | 1 | 1 | 1 | 1
 | 10 | 1 | 1 | 1 | 1

## Slide 40: Solve T5 as a POS Expression
Let’s solve T5. POS is better again.
What are the loops? for SOP?
(C3’ + C2’)
(C3’ + C1’ + C0’)
So T5 = (C3’ + C2’)· (C3’ + C1’ + C0’)
T5 |  | C3C2 |  |  | 
 |  | 00 | 01 | 11 | 10
C1C0 | 00 | 1 | 1 | 0 | 1
 | 01 | 1 | 1 | 0 | 1
 | 11 | 1 | 1 | 0 | 0
 | 10 | 1 | 1 | 0 | 1

## Slide 41: Combine T4 and T5 to find U(C)
How do we combine T4 and T5 to find the full upper-case checker function U(C)?
Remember:
  T4 applies when C6C5C4 = 100, and
  T5 applies when C6C5C4 = 101.
So …?
  AND T4 with C6C5’C4’,
  AND T5 with C6C5’C4, and
  OR the results together.

## Slide 42: A Good Solution, But Maybe We Can Do Less Work?
So U(C) = C6C5’C4’ (C3 + C2 + C1 + C0) + C6C5’C4 (C3’ + C2’)(C3’ + C1’ + C0’)
That’s a pretty small and fast solution.
But we still had to do a fair bit of work.
Is there an easier way?
Consider the following: to check for an upper-case letter, we need to know whether
C ≥ 1000001 AND C ≤ 1011010

## Slide 43: Use Two Comparators to Calculate U(C)
What about this approach?
Z0 = 1
implies
C < 0x41
Z1 = 1
implies
C > 0x5A
Notes: Explain the operation. Either implied condition means that U(C) is false. If both implied conditions are false, U(C) is true.

## Slide 44: Or Use Two Adders to Calculate U(C)
Or this approach?
Note that the adders are performing subtractions.
Notes: Remember that Cout = 0 for A – B means A < B.

## Slide 45: Inefficient, But Simple to Design
Quite large and slow compared with our first solution?
Consider two arguments:
  CAD tools can optimize away much of the extra overhead.
  Software executing on data center servers around the world executes the adder design even less efficiently, but it’s constantly in use on hundreds of thousands of machines.