## Slide 1: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Multiplexers (MUXes)

## Slide 2: Task: Checking for a Lower-Case Letter
What if we also need logic to check whether an ASCII character is a lower-case letter.
In ASCII, 'a' is 1100001 (0x61), and 'z' is 1111010 (0x7A).
Recall that 'A' is 1000001 (0x41), and 'Z' is 1011010 (0x5A).
Can we reuse our solutions for upper-case letters?
Of course we can!

## Slide 3: Change C5’ to C5 to Obtain L(C) from U(C)
Let’s again say that the ASCII character is in C = C6C5C4C3C2C1C0.
By breaking up the truth table, we obtained
U(C) = C6C5’C4’ (C3 + C2 + C1 + C0) + C6C5’C4 (C3’ + C2’)(C3’ + C1’ + C0’)
But lower-case characters are only different from upper-case in C5, which is 1 instead of 0.
L(C) = C6C5C4’ (C3 + C2 + C1 + C0) + C6C5C4 (C3’ + C2’)(C3’ + C1’ + C0’)

## Slide 4: Change Comparator Input to Calculate L(C)
Or just change the comparators’ inputs.
Z0 = 1
implies
C < 0x41
Z1 = 1
implies
C > 0x5A
0x61
0x61
L
0x7A
0x7A
Notes: Explain the operation. Either implied condition means that U(C) is false. If both implied conditions are false, U(C) is true.

## Slide 5: Want Logic to Choose Between Two Signals
What if we want one design to check for either upper-case or lower-case letters?
In a few examples,
  we added a control signal S
  to select between functions.
Can we design logic
  that uses a control signal S to select
  between two arbitrary signals, D1 (when S = 1) and D0 (when S = 0)?

## Slide 6: Truth Tables for a 2-to-1 Multiplexer
A full truth table for such logic appears to the right.
But we could shorten it as shown below…
S | D1 | D0 | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
S | D1 | D0 | Q
0 | x | 0 | 0
0 | x | 1 | 1
1 | 0 | x | 0
1 | 1 | x | 1
Unselected inputs do
not matter (marked
with “x”).
Notes: Talk about the full truth table before revealing the shortened version.

## Slide 7: We Normally Use the Most Compact Truth Table
In this case, we can even write outputs in terms of other inputs, as shown here.
S | Q
0 | D0
1 | D1
S | D1 | D0 | Q
0 | x | 0 | 0
0 | x | 1 | 1
1 | 0 | x | 0
1 | 1 | x | 1
Unselected inputs do
not matter (marked
with “x”).

## Slide 8: Expression for a 2-to-1 Multiplexer
Let’s solve with a K-map.
Q = S’D0 + SD1
S | D1 | D0 | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Q |  | D1D0 |  |  | 
 |  | 00 | 01 | 11 | 10
S | 0 |  |  |  | 
 | 1 |  |  |  | 
1
0
1
0
0
1
1
0
Notes: Fill in the K-map, then solve it.

## Slide 9: Expression for a 2-to-1 Multiplexer
But Q just selects D0 or D1 (as desired)!
Q = S’D0 + SD1
Could we have just written this expression using the table to the right? Q is D0 when S = 0, and D1 when S = 1…
S | Q
0 | D0
1 | D1

## Slide 10: Implementation and Symbolic Form of a 2-to-1 Mux
The circuit below shows a 2-to-1 mux (multiplexer), for which the symbolic form appears to the right.

## Slide 11: Selecting from More than Two Expressions
What if we want to select between four expressions, D3, D2, D1, and D0?
One answer is to use muxes hierarchically:
  start by using one 2-to-1 mux (signal S1)
  to decide between D3 or D2 and D1 or D0.
D3 or D2
D1 or D0

## Slide 12: For the Second Level, Use More Muxes
D3 or D2
D1 or D0
But how do we deliver two expressions to each mux input?
Use more muxes (both controlled by S0)!
Notice that S1S0 then allows us to choose from four expressions.

## Slide 13: AND Gates Represent Minterms ANDed with Data Inputs
For something as common as a mux, we typically build directly from gates.
Notice that each AND gate produces a minterm of S1, S0 ANDed with the corresponding Di.
D3S1S0
D2S1S0’
D1S1’S0
D0S1’S0’

## Slide 14: A 2N-to-1 Mux Requires N Select Bits
The diagram to the right shows the symbolic form of a 4-to-1 mux.
We can, of course, further extend this idea to build 8-to-1 muxes, 16-to-1 muxes, and so forth.
When selecting amongst P = 2N inputs DP-1 … D0 we need N bits of select input, SN-1 … S0.

## Slide 15: Can Use Sets of Muxes to Select Amongst Groups of Bits
We can also generalize the idea of multiplexers by
  using a common control signal
  to select between groups of inputs.
Generally,
  an N-to-M multiplexer
  represents M separate (N/M)-to-1 muxes
  each with log2(N/M) select bit inputs
  (typically N/M = 2K for some integer K).

## Slide 16: Example of a Set of Muxes with Common Select Input
For example, recall the design of the N-bit adder and subtractor.
We could have used a 2N-to-N mux
  to choose between Bi and Bi’ for the adder’s B input
  based on a common (one-bit) control signal S.
(Previously, we used the nature of the mux’ data inputs, Bi versus Bi’, to simplify each mux’ logic to an XOR gate.)

## Slide 17: Another Design Problem: Checking Four Types of ASCII
Now think again about our ASCII checker.
Say that we want four kinds of comparison:
  control characters (0x00 to 0x1F),
  lower-case letters (0x41 to 0x5A),
  upper-case letters (0x61 to 0x7A), and
  digits (0x30 to 0x39).
How can we design logic to check for any of the four types?

## Slide 18: The Answer? Use Muxes! Two 28-to-7 Muxes

## Slide 19: University of Illinois at Urbana-Champaign Dept. of Electrical and Computer Engineering ECE 120: Introduction to Computing
Decoders

## Slide 20: How Can We Decode a Representation?
What if we have
  designed a representation using N bits,
  and have an N-bit value in that representation,
  but need separate signals for each of the 2N possible bit patterns?
Applications include
  naming sets of bits, which we explore in 3-4 weeks, when we examine memory, and
  generating arbitrary functions dynamically, a technique used for many years in reconfigurable hardware devices.
Notes: … and homework. What a motivation.

## Slide 21: A Decoder’s Outputs Have Exactly One 1 Bit
In other words,
  given a set of N bits,
  we want to generate a signal for each possible combination of the N bits.
These signals correspond to the minterms on the N bits.
Exactly one of the resulting signals has the value 1.

## Slide 22: A 2-to-4 Decoder with Enable Produces Zero or One 1 Bit
We call the logic to perform such a task a decoder.
An example of a 2-to-4 decoder is shown to the right.
The decoder here has an enable signal. If EN = 0, all outputs are 0.

## Slide 23: A Trapezoid that Widens Represents a Decoder
The symbolic form for a decoder is a trapezoid.
  The N-bit signal to be decoded enters from the smaller side.
  The 2N outputs exit from the larger side.
If the decoder has an enable signal, it is typically drawn on a small side of the trapezoid.

## Slide 24: Decoders and Muxes Both Calculate All Minterms
Notice that the internal structure of a decoder looks similar to that of a mux.
In a mux, minterms are combined with per-minterm inputs and ORed together in a single output.

## Slide 25: Decoder Outputs Allow Separate Use of Each Minterm
The decoder allows the minterm signals to be used separately.
For example, each decoder output might control the mechanical release for a different product in a vending machine.

## Slide 26: Early Reconfigurable Hardware Used Decoders
Or we can use a decoder
  to compose arbitrary functions on the inputs
  by ORing together the right set of minterms.
Doing so is equivalent to composing a function with a mux by connecting 0s and 1s to its inputs.
But a single decoder can be used construct many functions, while the mux allows only one function.
Such an approach allowed
  programmable logic arrays (PLAs)
  to dynamically produce arbitrary functions,
  thus providing reconfigurable hardware.